November 4, 2014

Optimized software and hardware that convince

SAMAG presents the TFZ 2-1000 deep drilling & milling center live at EuroMold 2014

The TFZ production series handles all the requirements of a deep drilling & milling center. To meet market and client requirements, the TFZ production series has been expanded by two sizes in travel ranges and dimensions of the NC rotary tables. Moreover, the main focus was on improving the drilling and milling performance, the software applications and machine safety.

Higher speeds and torques also entail higher risks in the case of collisions. That’s why machine safety solutions for deep-hole drilling and milling centers are also a priority in Frankfurt. With the help of the exhibited TFZ 2-1000 we present the integrated machine AIRBAG from Engineering3D in action. It protects the deep-drilling & milling center and its spindles in crash situations by means of 3D acceleration sensor technology, which in the event of collisions triggers a full braking in less than a millisecond. Severe deformation and damages are thus prevented in critical cases. Additional options supplement the safety concept. For example the additional security prompt prevents a potential collision of the drilling and milling spindle with the chip box cartridge and the steady rests. The dynamic collision monitoring (DCM) detects imminent collisions of the tool and stops the corresponding axis with an error message. The Quick Check Kinematics function (QCK) measures and corrects the kinematic accuracy of the machine. Attendees can also see the manifold possibilities of the 3D CAM system GIBcam-DRILL, which the Dresdner Gesellschaft für Industrieberatung developed.

(1.722 Zeichen inkl. Leerzeichen)

The SAMAG TFZ 2-1000 in overview

| Large travel ranges |  |
| --- | --- |
| X-axis: | 1,200 mm |
| Y-axis: | 1,050 mm |
| Z-axis: | 1,100 mm |
| W-axis: | 1,600 mm |
| with NC rotary table: | 1,100 x 1,100 mm |
| max. drilling depth in one step: | 1,000/1,250 mm |
| max. bore diameter: | 4 - 30 mm |
| Milling capacity, material 1.2312: | 700 cm3/min |

SAMAG at EuroMold from 11/25 – 11/28/2014 in Hall 8, Booth J70

Caption:

Samag_pm_euromold2014_TFZ.jpg: At EuroMold 2014 SAMAG demonstrates the machine safety of the deep-hole drilling and milling centers with the assistance of a TFZ 2-1000

Download Area: http://www.koehler-partner.de/downloads/presseservice/

Public Relations Department:

KÖHLER + PARTNER GmbH

Am Flidderberg 48 ( D-21256 Handeloh

Phone +49 (0) 4188 8921-0 ( Fax +49 (0) 4188 8013

info@koehler-partner.de ( www.koehler-partner.de